## Slide 1
Workshop on Revised TEN-T Regulation, New KPIs, and Core Corridor Study
Introduction of New KPIs – Road transport
Brussels, 03 December 2024
Marivaux Hotel
Marcin Wójcik
European Commission DG MOVE B1

## Slide 2: Road transport
  Overall vision:
  To ensure high-quality roads and increase road safety
  To this aim:
  definition of minimum requirements for quality roads, safe and secure parkings and rest areas

## Slide 3: Road transport: key provisions (I)
  Member States shall ensure that:
  the roads are designed, built and maintained with a high level of environmental protection
  the roads are designed, built and maintained with high safety standards
  the safety of road transport infrastructure is ensured in accordance with Directive 2008/96/EC (Directive on road infrastructure safety management)
  road tunnels over 500 m comply with Directive 2004/54/EC (Directive on road tunnels)
  the interoperability of toll collection systems is ensured in accordance with Directive (EU) 2019/520 (Directive on interoperability of road toll systems) and Directive 1999/62/EC (Directive on charging of heavy goods vehicles)
  any intelligent transport system on road transport infrastructure complies with Directive 2010/40/EU (ITS Directive)
  alternative fuels infrastructure is deployed on the road network in accordance with Regulation (EU) 2023/1804 (AFIR)

## Slide 4: Road transport: key provisions (II)
  Roads shall provide, separate carriageways for the two directions of traffic and not cross at grade with any road, railway, tram track, bicycle or footpath on the core network by 2030 and extended core network by 2040.
  Weigh in motion systems should be deployed every 300 km on average on the core and extended core network by 2040 and on the comprehensive network by 2050
  Rest areas shall be developed every 60 km on the core and extended core network by 2040 and every 100 km on the comprehensive network by 2050

## Slide 5: Road transport: key provisions (III)
  Safe and secure parking areas shall be developed every 150 km on average on core and extended core network (or within 3 km driving distance from the nearest exit) by 2040 - in coherence with refueling obligations as per AFIR since TEN-T parkings would be ideal spot to place the charging stations
  Means to detect safety-related events or conditions shall be deployed, and road traffic data to provide road safety-related traffic information shall be collected (on the core network by 2030, extended core network by 2040, the comprehensive network by 2050 at the latest)

## Slide 6: Road transport: exemptions
  At the request of a Member State, in duly justified cases, the Commission adopts implementing acts granting exemptions from the requirement with respect to roads where the traffic density does not exceed 10 000 vehicles per day in both directions, or on grounds of specific geographical or significant physical constraints, negative result of socio-economic cost-benefit analysis or significant negative impacts on environment or biodiversity.
  The request for exemptions should be coordinated with the neighbouring Member States where applicable.

## Slide 7: Thank you
TENtec interactive map viewer:
https://ec.europa.eu/transport/infrastructure/tentec/tentec-portal/map/maps.html