## Slide 1
Development of indicative TEN- T extensions of the Comprehensive and Core Network in Western Balkans
04.12.2024
Notes: 4th Annual TEN-T report
Annual report included the revised TEN-T network as per new Regulation
Still using the existing KPIs, new KPIs to be monitored next year
Progress - key TEN-T indicators - remained steady, and even accelerated.

## Slide 2: Rail network
Notes: 5853 km in total
2700 km WB

## Slide 3: Rail network – Compliance with KPIs
Chart: Percentages of electrified and non-electrified lines 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
electrified | 0.7304 | 0.7398 | 0.7157 | 0.65094 | 0.5434 | 0.5554 | 0.5206 | 0.55343
non electrified | 0.2696 | 0.2602 | 0.2843 | 0.35253 | 0.4566 | 0.4445 | 0.4794 | 0.44661

## Slide 4
Chart: Axle load in tonnes/axle on Core and Comprehensive Network 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
22.5 t/axle | 0.8743 | 0.8888 | 0.8844 | 0.8388 | 0.7213 | 0.7452 | 0.6996 | 0.7349
less than 22,5 t/axle | 0.1257 | 0.1112 | 0.1156 | 0.1612 | 0.2787 | 0.2547 | 0.3004 | 0.2651
Rail network – Compliance with KPIs

## Slide 5: Rail network – Compliance with KPIs
Chart: Design Speed 100 km/h and over 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
compliant | 0.7199 | 0.7957 | 0.7885 | 0.60323 | 0.6069 | 0.6766 | 0.6815 | 0.58984
non compliant | 0.2801 | 0.2043 | 0.2115 | 0.39677 | 0.3931 | 0.3233 | 0.3185 | 0.41016
Chart: Operating Speed 100 km/h and over for 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
compliant | 0.1455 | 0.1358 | 0.1579 | 0.1724 | 0.1279 | 0.1237 | 0.1375 | 0.1453
non compliant | 0.8545 | 0.8642 | 0.8423 | 0.8276 | 0.8721 | 0.8762 | 0.8625 | 0.8547

## Slide 6
Rail network – Compliance with KPIs
Chart: Train length 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
min 740 m | 0 | 0 | 0.0344 | 0.1589 | 0 | 0 | 0.0225 | 0.1466
less than 740 m | 1 | 1 | 0.9657 | 0.8411 | 1 | 1 | 0.9775 | 0.8534

## Slide 7
Rail network – Compliance with KPIs
Rail network – Compliance with KPIs
Chart: ERTMS deployment 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
compliant | 0 | 0.0271 | 0.0263 | 0.021974 | 0 | 0.0239 | 0.0172 | 0.016255
non compliant | 1 | 0.9729 | 0.9737 | 0.97803 | 1 | 0.9761 | 0.9828 | 0.98374

## Slide 8
Chart: Condition of the Rail Network 2021/2022/2023/2024
| 2021 | 2022 | 2023 | 2024 | 2021 | 2022 | 2023 | 2024 | Core | Comprehensive
Very good | 0.1338 | 0.0997 | 0.0983 | 0.16201 | 0.1574 | 0.164 | 0.1053 | 0.13552
Good | 0.1673 | 0.3324 | 0.3032 | 0.22484 | 0.123 | 0.2587 | 0.2756 | 0.2731
Average | 0.2611 | 0.1272 | 0.174 | 0.14882 | 0.2694 | 0.133 | 0.1563 | 0.13773
Poor | 0.0946 | 0.1502 | 0.0445 | 0.040014 | 0.0635 | 0.1439 | 0.0443 | 0.0296
Very poor | 0.3432 | 0.2905 | 0.38 | 0.42453 | 0.3866 | 0.3005 | 0.4184 | 0.42414
Rail network – Conditions

## Slide 9: Rail network – Ongoing projects
18 ongoing rail projects
(18 on the Core Network, 0 on the Comprehensive Network)
965 km of rail new/rehab
(965km on the Core Network, 0 km on Comprehensive Network)
3.612 billion EUR committed
(3.612 billion EUR for the Core Network)

## Slide 10: Rail network – Planned projects
7 projects mature (329 km)
15 projects under preparation (1402 km)
€2.01 bn mature
€8.44 bn under preparation
0 projects mature (0 km)
5 projects under preparation (310 km)
€0 ml mature
€950 ml under preparation
€11.4 billion

## Slide 11: Rail network – Conditions 2027
Chart: Condition of the Rail Network 2021/2022/2023/2024 and Forecast for 2027
| 2021 | 2022 | 2023 | 2024 | 2027 | 2021 | 2022 | 2023 | 2024 | 2027 | Core | Comprehensive
Very good | 0.1338 | 0.0997 | 0.0983 | 0.16201 | 0.39188 | 0.1574 | 0.164 | 0.1053 | 0.13552 | 0.31384
Good | 0.1673 | 0.3324 | 0.3032 | 0.22484 | 0.21426 | 0.123 | 0.2587 | 0.2756 | 0.2731 | 0.26696
Average | 0.2611 | 0.1272 | 0.174 | 0.14882 | 0.11316 | 0.2694 | 0.133 | 0.1563 | 0.13773 | 0.1051
Poor | 0.0946 | 0.1502 | 0.0445 | 0.040014 | 0.013299 | 0.0635 | 0.1439 | 0.0443 | 0.0296 | 0.01002
Very poor | 0.3432 | 0.2905 | 0.38 | 0.42453 | 0.2674 | 0.3866 | 0.3005 | 0.4184 | 0.42414 | 0.30409

## Slide 12: Growth Plan for Western Balkans – Reform Agenda
ITS
MAIC
Regional market opening
National Bodies
RRA, NIB, NSA
Legislation and Institutions
Investment Priorities
Albania – Corridor VIII
Kosovo – Route 10
Montenegro – Route 4
North Macedonia – Corridor VIII, X

## Slide 13
Thank you for your attention!
dlasica@transport-community.org