## Slide 1: Integration of DG in the SMS Role of the safety advisor
22nd TC on DG| 18 JUNE 2026

## Slide 2: Role actors developing & improving railway safety (IM/RU) 1/2
DIRECTIVE (EU) 2016/798 of 11 MAY 2016 on railway safety (RSD)
(EUR-Lex – 32016L0798 - EN - EUR-Lex)
ART. 4 (3)
Railway undertakings and infrastructure managers shall:
implement the necessary risk control measures referred to in point (a) of Aritcle 6(1), where appropriate in cooperation with each other and with other actors;
take consider in their safety management systems of the risks associated with the activities of other actors and third parties;
where appropriate, contractually oblige the other actors referred to in paragraph 4 having a potential impact on the safe operation of the Union rail system to implement risk control measures; and
ensure that their contractors implement risk control measures through the application of the CSMs for monitoring processes set out in the CSMs on monitoring referred to in point (c) of Article 6(1), and that this is stipulated in contractual arrangements to be disclosed on request of the Agency or of the national safety authority

## Slide 3: Role actors developing & improving railway safety (IM/RU) 2/2
DIRECTIVE (EU) 2016/798 of 11 MAY 2016 on railway safety (RSD)
(EUR-Lex – 32016L0798 - EN - EUR-Lex)
ART. 4 (4):
Without prejudice to the responsibilities of RU’s & IM’s, ECMs and all other actors having impact on the safe operation of the Union rail system, including manufacturers, maintenance suppliers, keepers, service providers, contracting entities, carriers, consignors, consignees, loaders, unloaders, fillers and unfillers shall:
implement the necessary risk control measures, where appropriate in cooperation with other actors;
ensure that subsystems, accessories, equipment and services supplied by them comply with specified requirements and conditions for use so that they can be safely operated by the railway undertaking and/or the infrastructure manager concerned
Art. 4 (5):
Railway undertakings, infrastructure managers and any actor referred to in paragraph 4 who identifies or is informed of a safety risk relating to defects and construction non-conformities or malfunctions of technical equipment, including those of structural subsystems, shall, within the limits of their respective competence:
- take any necessary corrective measure to tackle the safety risk identified;
- report those risks to the relevant parties involved, in order to enable them to take any necessary further corrective action to ensure continuous achievement of the safety performance of the Union rail system. The Agency may establish a tool that facilitates this exchange of information among the relevant actors, taking into account the privacy of the users involved, the results of a cost-benefit analysis as well as the IT applications and registers already set up by the Agency
Notes: .

## Slide 4
Roles and obligations 15 EU relevant legislative texts interfacing with RID

## Slide 5: TSI OPE – Dangerous goods
COMMISSION REGULATION (EU) No 1078/2012 of 16 November 2012 on a common safety method for monitoring to be applied by railway undertakings, infrastructure managers after receiving a safety certificate or safety authorisation and by entities in charge of maintenance
(EUR-Lex – 02019RO773-20230928 - EN - EUR-Lex)
The Railway undertaking shall define the procedures to perform the transport of dangerous goods.
These procedures shall include:
The provisions as specified in Directive 2008/68/EC of the European Parliament and of the Council and Directive 2010/35/EU of the European Parliament and of the Council as applicable
Information to the driver of the presence and position of dangerous goods on the train
Information the infrastructure manager requires for transport of dangerous goods
Determination, in conjunction with the infrastructure manager, of lines of communication and planning of specific measures in case of emergency situations involving the goods.

## Slide 6: Safety Advisor
Interactions with dangerous goods legislation
facilitate the conduct of those activities in accordance with the requirements applicable and in the safest possible way.
Role of the adviser
– monitoring compliance with the requirements governing the carriage of dangerous goods;
– advising his undertaking on the carriage of dangerous goods;
– preparing an annual report on the activities in the carriage of dangerous goods.
Safety Management System | ERA (europa.eu)

## Slide 7: Safety Management System (SMS)
Directive (EU) 2016/798 (EUR-Lex - 32016L0798 - EN - EUR-Lex)
Article 9(3) The safety management system shall contain the following basic elements:
(a) a safety policy approved by the organisation's chief executive and communicated to all staff;
(b) qualitative and quantitative targets of the organisation for the maintenance and enhancement of safety, and plans and procedures for reaching these targets;
(c) procedures to meet existing, new and altered technical and operational standards or other prescriptive conditions as laid down in TSIs, national rules referred to in Article 8 and Annex II, other relevant rules or authority decisions;
(d) procedures to assure compliance with the standards and other prescriptive conditions throughout the life cycle of equipment and operations;
(e) procedures and methods for identifying risks, carrying out risk evaluation and implementing risk-control measures whenever a change of operating conditions or the introduction of new material imposes new risks on the infrastructure or the man-machine-organisation interface;
(f) the provision of programmes for the training of staff and systems to ensure that the staff's competence is maintained
and that tasks are carried out accordingly, including arrangements with regard to physical and psychological fitness;
(g) arrangements for the provision of sufficient information within the organisation and, where appropriate, between
organisations of the railway system;
(h) procedures and formats for the documentation of safety information and designation of procedure for the configuration control of vital safety information;
(i) procedures to ensure that accidents, incidents, near misses and other dangerous occurrences are reported, investigated and analysed and that necessary preventive measures are taken;
(j) the provision of actions plans, alerts and information in the event of an emergency, agreed upon with the appropriate public authorities; and
(k) provisions for recurrent internal auditing of the safety management system.
Infrastructure managers and railway undertakings shall include any other element necessary to cover safety risks, in accordance with the assessment of risks arising from their own activity.
Detailed requirements are established by
COMMISSION DELEGATED REGULATION (EU) 2018/762 of 8 March 2018 establishing common safety methods on safety management system requirements
(EUR-Lex - 32018R0762 - EN - EUR-Lex)
And by
COMMISSION IMPLEMENTING REGULATION (EU) 2019/773 of 16 May 2019 on the technical specification for interoperability relating to the operation and traffic management subsystem of the rail system within the European Union and repealing Decision 2012/757/EU
(EUR-Lex - 32019R0773 - EN - EUR-Lex)
Interactions with dangerous goods legislation
RID 1.8.3.3
The main task of the adviser shall be, under the responsibility of the head of the undertaking, to seek by all
appropriate means and by all appropriate action, within the limits of the relevant activities of that undertaking, to facilitate the conduct of those activities in accordance with the requirements applicable and in the safest possible way.
With regard to the undertaking’s activities, the adviser has the following duties in particular:
– monitoring compliance with the requirements governing the carriage of dangerous goods;
– advising his undertaking on the carriage of dangerous goods;
– preparing an annual report to the management of his undertaking or a local public authority, as appropriate, on the undertaking's activities in the carriage of dangerous goods. Such annual reports shall be preserved for five years and made available to the national authorities at their request
The adviser's duties also include monitoring the following practices and procedures relating to the relevant
activities of the undertaking:
– the procedures for compliance with the requirements governing the identification of dangerous goods being transported;
– the undertaking's practice in taking account, when purchasing means of transport, of any special requirements in connection with the dangerous goods being transported;
– the procedures for checking the equipment used in connection with the carriage, packing, filling, loading or unloading of dangerous goods;
– the proper training of the undertaking’s employees, including on the changes to the regulations, and the maintenance of records of such training;
– the implementation of proper emergency procedures in the event of any accident or incident that may affect safety during the carriage, packing, filling, loading or unloading of dangerous goods;
– investigating and, where appropriate, preparing reports on serious accidents, incidents or serious infringements recorded during the carriage, packing, filling, loading or unloading of dangerous goods;
– the implementation of appropriate measures to avoid the recurrence of accidents, incidents or serious infringements;
– the account taken of the legal prescriptions and special requirements associated with the carriage of dangerous goods in the choice and use of sub-contractors or third parties;
– verification that employees involved in the consigning, carriage, packing, filling, loading or unloading of dangerous goods have detailed operational procedures and instructions,
– the introduction of measures to increase awareness of the risks inherent in the carriage, packing, filling, loading and unloading of dangerous goods;
– the implementation of verification procedures to ensure the presence on board means of transport of the documents and safety equipment which must accompany transport and the compliance of such documents and equipment with the regulations;
– the implementation of verification procedures to ensure compliance with the requirements governing packing, filling, loading and unloading;
– the existence of the security plan indicated in 1.10.3.2.

## Slide 8: What is monitoring?
COMMISSION REGULATION (EU) No 1078/2012 of 16 November 2012 on a common safety method for monitoring to be applied by railway undertakings, infrastructure managers after receiving a safety certificate or safety authorisation and by entities in charge of maintenance
(EUR-Lex - 32012R1078 - EN - EUR-Lex)
The monitoring process is an iterative process of the management system:
it enables to verify if the application of the management system is correct and if the expected outcomes, including the company safety targets, are met. If not, the monitoring process requires to take corrective and/or preventive measures and, in the next cycle of the monitoring activities, to verify if these new measures bring the proposed improvements or if further new measures need to be considered.

## Slide 9: Monitoring of SMS effectiveness
Interactions with dangerous goods legislation
RID 1.8.3.3
The main task of the adviser shall be, under the responsibility of the head of the undertaking, to seek by all appropriate means and by all appropriate action, within the limits of the relevant activities of that undertaking, to facilitate the conduct of those activities in accordance with the requirements applicable and in the safest possible way.
With regard to the undertaking’s activities, the adviser has the following duties in particular:
– monitoring compliance with the requirements governing the carriage of dangerous goods;
– advising his undertaking on the carriage of dangerous goods;
– preparing an annual report to the management of his undertaking or a local public authority, as appropriate, on the undertaking's activities in the carriage of dangerous goods. Such annual reports shall be preserved for five years and made available to the national authorities at their request.
The adviser's duties also include monitoring the following practices and procedures relating to the relevant
activities of the undertaking:
– the procedures for compliance with the requirements governing the identification of dangerous goods being transported;
– the undertaking's practice in taking account, when purchasing means of transport, of any special requirements in connection with the dangerous goods being transported;
– the procedures for checking the equipment used in connection with the carriage, packing, filling, loading or unloading of dangerous goods;
– the proper training of the undertaking’s employees, including on the changes to the regulations, and the maintenance of records of such training;
– the implementation of proper emergency procedures in the event of any accident or incident that may affect safety during the carriage, packing, filling, loading or unloading of dangerous goods;
– investigating and, where appropriate, preparing reports on serious accidents, incidents or serious infringements recorded during the carriage, packing, filling, loading or unloading of dangerous goods;
– the implementation of appropriate measures to avoid the recurrence of accidents, incidents or serious infringements;
– the account taken of the legal prescriptions and special requirements associated with the carriage of dangerous goods in the choice and use of sub-contractors or third parties;
– verification that employees involved in the consigning, carriage, packing, filling, loading or unloading of dangerous goods have detailed operational procedures and instructions,
– the introduction of measures to increase awareness of the risks inherent in the carriage, packing, filling, loading and unloading of dangerous goods;
– the implementation of verification procedures to ensure the presence on board means of transport of the documents and safety equipment which must accompany transport and the compliance of such documents and equipment with the regulations;
– the implementation of verification procedures to ensure compliance with the requirements governing packing, filling, loading and unloading;
– the existence of the security plan indicated in 1.10.3.2.
Directive (EU) 2016/798 (EUR-Lex - 32016L0798 - EN - EUR-Lex)
Article 6(1)(c) is requiring the establishment of (c) the methods for supervision to be applied by national safety authorities and the methods for monitoring to be applied by railway undertakings, infrastructure managers and entities in charge of maintenance;
The method for monitoring is provided by
COMMISSION REGULATION (EU) No 1078/2012 of 16 November 2012 on a common safety method for monitoring to be applied by railway undertakings, infrastructure managers after receiving a safety certificate or safety authorisation and by entities in charge of maintenance
(EUR-Lex - 32012R1078 - EN - EUR-Lex)
Note: the scope of application of this regulation is not fully matching with the scope of activities of safety advisors and does not cover security plans in accordance with RID.
In particular, it is applicable to the monitoring of activities for which the railway undertaking, railway infrastructure manager, entity in charge of maintenance are responsible.

## Slide 10: Safety obligations carrier Monitoring the correct implementation of activities relating to carriage of dangerous goods
Responsibilities of the carrier to control the risks that arise from activities relating to DG:
Ascertain that the DG to be carried are authorized for carriage;
Ascertain that
  all the information prescribed in RID related to the DG to be carried has been provided by the consignor before carriage;
  The prescribed documentation is attached to the transport document;
  If EDP or EDI technics are used instead of paper documentation, that data is available during transport in a manner at least equivalent to that paper documentation
Ascertain visually that the wagons and loads have no obvious defects, leakages or cracks, missing equipment, etc.;
Ascertain that the data specified for the next inspection for tank-wagons, battery-wagons, wagons with demountable tanks, portable tanks, tank-containers and MEGCs has not expired;
Verify that the wagons are not overloaded
Ascertain that the placards, marks and orange-coloured plates prescribed for wagons in Chapter 5.3 of RID have been affixed;
Ascertain that the equipment prescribed in the instructions in writing is in the driver’s cab

## Slide 11: Safety obligations carrier Monitoring the correct implementation of activities relating to carriage of dangerous goods
Responsibilities of the carrier to control the risks that arise from activities relating to DG:
Shall ensure that the IM being use is able to obtain at any time during carriage rapid and unrestricted access to the information allowing him to meet the information related to the dangerous goods;
Shall provide the driver with the written instructions as prescribed in chapter 5.4.3 of RID;
Shall inform the driver of the DG on board and their position on the train before the train starts its journey;

## Slide 12: Safety obligations of the participants Supply chain responsibility
To the nature and the extend of foreseeable dangers
To avoid damage and injury
To minimize their effects
 Comply with RID requirements in their respective fields
Participants in the carriage of dangerous goods shall take appropriate measures according:

## Slide 13: THANK YOU
Moving Europe towards a sustainable and safe railway system without frontiers.
Follow us: